# MegapixelCam

Experience the highest quality, full screen color images available anywhere with this feature-rich

construction camera system

EarthCam 6 MegapixelCam Specification  	                                         A&E Short Form*

- Physical

Dimensions: 10.55” W x 6.19” H x 26.5” L (26.79cm W x 15.72cm H x 67.31cm L)

Weight: 16 lbs (7.26 kg)

- Environmental

Operational Temperature: -10°F to 120°F (-23°C to 49°C)

Thermostatically Controlled Heater and Blower

24/7 Operation in All Weather Conditions

- Construction

Powder Coated Aluminum Housing with Stainless Steel Fittings for Padlocks

Impact Resistant Viewing Window, 0.25” (6.35mm) Thick

Two UL Rated Compression Glands, Gas Spring Lid, Adjustable Camera Sled

- Camera

Imager: 6.3 Megapixel, 22.0mm x 14.7mm CMOS

Lens: F-Stop: F/3.5 – F/5.6, 18mm – 55mm, 3x Optical

Resolutions: 3088 x 2056 Pixels = 6 Megapixels

Auto Features:  ISO, Shutter, White Balance and Focus

Compression: Motion JPEG

Communication: 10base-T/100base-TX Ethernet, IP Addressing: Dynamic or Static

Designed For “EarthCam Control Center - Megapixel Edition – Fixed with Mobile Support” Software

- Electrical

Operational Voltage: 120VAC (230VAC Available). Power Consumption: 130W

# Interface and Online Software Features

Software Delivered by Vendor as a Managed Service

Displays Company Logo and Project Name

Capable of Viewing Actual Live Video

Calendar Based Navigation System for Selecting Specific Images

Multifunction Image Browsing

Pan, Tilt and Zoom Capability within a High Definition Image

A Multiview Screen to View All Cameras on Project at the Same Time

Graphical Mark-Up Tools for Detailing and Creating Overlays on Images

Graphical Weather Applet Displaying Ten Points of Local Weather Data and 48-hour Forecast

Remote Solar Monitoring Screen Displaying the DC Amperage Output of Solar Panels

Remote Battery Monitoring Screen Displaying Battery Voltage, Temperature and Status

Remote Cellular Monitoring Screen Displaying Connectivity, Network Traffic and Modem Temperature

Remote Wireless Radio Monitoring Screen Displaying Connectivity, Network Traffic and

Google Map Features Including Wireless Radio Locations

Share Image Tools: Save, Print, Email and Post to Message board or Mobile Devices

Automated Progress Report in PowerPoint, Open Office and PDF Formats

Map, Aerial and Satellite View by Google

Time-Lapse Feature Includes – Instant Time-Lapse Play Back by Day, Week, Month or Year

Machine to Machine Self-Healing Technology Automates Maintenance of Camera Up to 288 Times Daily

Account Security Features Include – Four Levels of Password Protection, IP Address Block/ Permission and SSL Protection of User Login Password

All Images are the Copyright of the Client and Protected on Secure Servers Owned and Operated by the System Vendor

# Text boxes

### Product Features

The industry standard for megapixel cameras designed for projects

of any length and budget.

· 6.3 megapixel HD fixed position camera

· Large high-definition images: 3088 x 2056 pixels

· Digital presets and Pan/Tilt/Zoom within captured image

· Take instant live snapshot in addition to 15 minutes archives

· Heavy-duty, temperature controlled enclosure

· Unique double locking mount for jitter-free documentation

· Fast, dependable, solid state Linux system

· 3G, 4G, Wi-Fi and microwave options available

· Available in Wide Angle and Skyscraper versions

#### Architectural & Engineering Specifications

#### Product:  ECCS03103

#### Revised:  09-12-2012

#### DOWNLOAD ELECTRONIC VERSION OF THIS SPECS

#### http://www.earthcam.net/aespecs/megapixelcam

For additional EarthCam A&E specs visit: http://www.earthcam.net/aespecs/systems