# ConstructionCam Lite

Your entry-level Pan/Tilt/Zoom construction camera to monitor smaller projects and view your construction site live.

# EarthCam ConstructionCam Lite Specification   	                          A&E Short Form*

## Physical

Dimensions: 6.3” H x 7.4” W (15.9cm H x 18.8cm W)

Weight: 2.6lbs (1.2Kg)

- Environmental

Operation Temperature: -4°F to +122°F (-20°C to +50°C)

Thermostatically Controlled Heater

- Construction

The indoor/outdoor camera system consists of an IP66 weather resistant aluminum and plastic housing

with an acrylic optically clear dome to be mounted on a fixed pole, wall, parapet or ceiling.

- Camera

Image Sensor:  1/4” CCD

Frame rate: H.264 up to 30/25 fps in all resolutions. Motion JPEG: up to 30/25 fps in all resolutions.

Minimum Illumination: Color 1 lux at 30 IRE F1.6, B/W 0.3 lux at 30IRE F1.6.

Video Compression: H.264 (MPEG-4 Part 10/AVC) Motion JPEG

Resolution: 704 x 480

Lens: 3.8mm – 46mm, Zoom: 12x optical, 4x digital.

Image Settings: Day/Night, White Balance, Color, Brightness, Sharpness, Backlight Compensation

Pan Range: 360º, Tilt Range: 180º

Communication: 10BASE-T/100BASE-TX Ethernet, IP Addressing: Dynamic or Static

Designed For "EarthCam Control Center - Streaming Edition" Software

- Electrical

Operational Voltage: 120VAC, Maximum power consumption: 15.6W

(using Power Over Ethernet(IEEE 802.3af Class 3))

# Interface and Online Software Features

Software Delivered by Vendor as a Managed Service

Displays Company Logo and Project Name

Capable of Viewing Actual Live Video

Robotic Pan, Tilt, Zoom Control of Camera System

Calendar Based Navigation System for Selecting Specific Images

Multifunction Image Browsing

A Multiview Screen to View All Cameras on Project at the Same Time

Graphical Mark-Up Tools for Detailing and Creating Overlays on Images

Graphical Weather Applet Displaying Ten Points of Local Weather Data and 48-hour Forecast

Remote Solar Monitoring Screen Displaying the DC Amperage Output of Solar Panels

Remote Battery Monitoring Screen Displaying Battery Voltage, Temperature and Status

Remote Cellular Monitoring Screen Displaying Connectivity, Network Traffic and Modem Temperature

Remote Wireless Radio Monitoring Screen Displaying Connectivity, Network Traffic and

Google Map Features Including Wireless Radio Locations

Share Image Tools: Save, Print, Email and Post to Message board or Mobile Devices

Automated Progress Report in PowerPoint, Open Office and PDF Formats

Map, Aerial and Satellite View by Google

Time-Lapse Feature Includes – Instant Time-Lapse Play Back by Day, Week, Month or Year

Machine to Machine Self-Healing Technology Automates Maintenance of Camera Up to 288 Times Daily

Account Security Features Include – Four Levels of Password Protection, IP Address Block/ Permission and SSL Protection of User Login Password

All Images are the Copyright of the Client and Protected on Secure Servers Owned and Operated by the System Vendor

# Text boxes

### Product Features

Good balance of performance and price.

· Remote Pan/Tilt/Zoom controls with multiple preset compositions
· 12x optical, 4x digital zoom with pan angle of 360°
· Automatic day and night function
· Multi-stream H.264 and Motion JPEG

· All weather dome housing with heater & fan
· Fast, dependable, solid state Linux system
· Lightweight and easy to install
· Inexpensive and reliable webcam
· Streaming video over 4G wireless networks

· Fully assembled

#### Architectural & Engineering Specifications

#### Product:  ECCS05100

Revised:  12-24-2013

#### DOWNLOAD ELECTRONIC VERSION OF THIS SPECS

#### http://www.earthcam.net/aespecs/constructioncamlite

For additional EarthCam A&E specs visit: http://www.earthcam.net/aespecs/systems