# Mobile TrailerCam Advanced

Rugged, self-powered trailer features a live robotic dome camera and optional digital detection equipment to analyze and manage traffic.

EarthCam Mobile TrailerCam Advanced Specification   	                      A&E Short Form*

- Physical

Traveling Dimensions: 15’ L x 7’ W x 7’ H (4.6m L x 2.1m W x 2.1m H)

Weight: 2800lbs (1270kg)

- Construction

Single Torsion-type Axle Steel Welded Trailer with 2” Adjustable Ball Hitch Manual Outriggers

DOT Approved Lighting Package to Include Brake and Marker Lights

Trailer Mounted Locking Manual/Motorized 42-Foot Mast with Spiral Conduit for Cable Deployment

Full Size Spare Tire
Guy Wires: To Stabilize an Extended Mast and Steady the Camera Shot

- Battery Bank

Charge Controller with Remote Monitoring

Battery Type: Twelve 6Volt DC Deep Cycle Batteries

45 Amp AC Battery Charge

- Solar Array

Single Crystal (monocrystalline) Silicon Photovoltaic Modules

Region of Operation: Contiguous United States

Autonomy: 4 Days Battery Backup

- Camera

All Aluminum Camera Housing with an Impact Resistant Acrylic Dome

Imager: 1/4" EXview HAD, Sensitivity: 0.00018 lux B/W, 0.55 lux Color, 540 TV Lines

Lens: F-Stop: F/1.4, Motorized Zoom: 3.4mm – 119mm, 35x Optical, 12x Digital, Image Stabilization

Auto Features:  Shutter and Low Shutter Modes, White Balance, Focus

Pan/Tilt: Pan Range: 360° Continuous at Speed of 0.1º-80°/s, Tilt Range: +2° to -92° at Speed of 0.1°-40°/s

# EarthCam Webcaster

Single Channel Video Server Webcaster 5001, Frames Per Second: 30fps, Compression: Motion JPEG, MPEG

Events Triggered by Motion Detection, External Inputs or Schedule and Alarm Notification Via E-mail,

TCP, HTTP

Communication: 10Base-T/100Base-TX Ethernet, IP Addressing: Dynamic or Static

### Designed for “EarthCam Control Center – Streaming Video Edition – Robotic with Mobile Support” Software

# Communication

Wireless GPS Modem EV–DO Rev.A Full Duplex Transceiver with Dual-Band Support for Both 800 MHz Cellular and

1.9 GHz PCS Bands. Forward Link Up to 3.1 Mbps; Reverse Link 1.8 Mbps and Real Time GPS Reporting

# Interface and Online Software Features

Software Delivered by Vendor as a Managed Service

Displays Company Logo and Project Name

## Capable of Viewing Actual Live Video

Picture in Picture to View and Control Live Video, While Viewing Additional Data

Robotic Pan, Tilt, Zoom Control of Camera System

Calendar Based Navigation System for Selecting Specific Images

##### Multifunction Image Browsing

##### Pan, Tilt and Zoom Capability within a High Definition Image

A Multiview Screen to View All Cameras on Project at the Same Time

Graphical Mark-Up Tools for Detailing and Creating Overlays on Images

Graphical Weather Applet Displaying Ten Points of Local Weather Data and 48-hour Forecast

Remote Solar Monitoring Screen Displaying the DC Amperage Output of Solar Panels

Remote Battery Monitoring Screen Displaying Battery Voltage, Temperature and Status

Remote Cellular Monitoring Screen Displaying Connectivity, Network Traffic and Modem Temperature

Remote Wireless Radio Monitoring Screen Displaying Connectivity, Network Traffic and

Google Map Features Including Wireless Radio Locations

Share Image Tools: Save, Print, Email and Post to Message Board or Mobile Devices

Automated Progress Report in PowerPoint, Open Office and PDF Formats

Map, Aerial and Satellite View by Google

#### Time-Lapse Feature Includes – Instant Time-Lapse Play Back by Day, Week, Month or Year

Machine to Machine Self-Healing Technology Automates Maintenance of Camera Up to 288 Times Daily

Account Security Features Include – Four Levels of Password Protection, IP Address Block/ Permission and SSL Protection of User Login Password

All Images are the Copyright of the Client and Protected on Secure Servers Owned and Operated by the System Vendor

# Text boxes

### Product Features

Our best remote traffic monitoring system.

· Standalone wireless and self powered system is easy to deploy and setup
· Robotic HD streaming 360° dome camera with 20x optical zoom
· GPS 3G/4G modem or WiFi
· 42' mast extension
· 150 Watt solar panels, EFOY fuel cell capable
· AGM sealed battery with disconnect switch, 75 Amp battery charger
· Full size spare tire and removable tongue
· Guy Wires to stabilize an extended mast and steady the camera shot
· Real-time remote data management
· Fast, dependable, solid state Linux system
· Custom branding to display your company logo

· Lease or purchase

#### Architectural & Engineering Specifications

#### Product:  ECCS09204

#### Revised:  05-06-2011

#### DOWNLOAD ELECTRONIC VERSION OF THIS SPECS

#### http://www.earthcam.net/aespecs/trailercamadvanced

For additional EarthCam A&E specs visit: http://www.earthcam.net/aespecs/systems