# Mobile TrailerCam Lite

EarthCam's lite model trailer provides self-generated solar power and wireless communications

for rapid deployment and secure transmission.

EarthCam Mobile TrailerCam Lite Specification   	 	                         A&E Short Form*

- Physical

Dimensions: 12’ L x 6’ W x 10’ H (3.66m L x 1.82m W x 3m H)

Weight: 2800lbs (1270kg)

- Construction

Single Torsion-type Axle Steel Welded Trailer with 2” Adjustable Ball Hitch and Telescoping Manual Outriggers

DOT Approved Lighting Package to Include Brake and Marker Lights

Trailer Mounted Locking Manual/Motorized 30-Foot Mast with Spiral Conduit for Cable Deployment

- Battery Bank

Charge Controller with Remote Monitoring

Battery Type: Twelve 6Volt DC Deep Cycle Batteries

45 Amp AC Battery Charge

- Solar Array

Single Crystal (monocrystalline) Silicon Photovoltaic Modules

Region of Operation: Contiguous United States

Autonomy: 4 Days Battery Backup

- Camera

Engineered Plastic Upper Dome with Aluminum Wall Mounting Bracket and High-impact, Optically Clear, UV Protected Polycarbonate Lower Dome with Thermostatically Controlled Heater and Defroster

Imager: 1/4" CCD, 1 Lux @ F/1.6

Compression: Motion JPEG / MPEG4

Lens: F-Stop: F/1.6 – F/2.7, Motorized Zoom: 3.8mm – 46mm, 12x Optical, 4x Digital

Resolution: 704 x 480 pixels

Frames Per Second: Maximum 30fps at 4 CIF

Auto Features: Iris, Focus, White Balance, Backlight Compensation, Day/Night Function

Pan/Tilt: Pan Range: +170º to -170º, Tilt Range: 180º

Communication: 10Base-T/100Base – TX Ethernet, IP Addressing: Dynamic or Static

Designed for “EarthCam Control Center – Streaming Video Edition – Robotic with Mobile Support” Software

## Communication

Wireless Modem EV–DO Rev.A Full Duplex Transceiver with Dual-Band Support for Both 800 MHz Cellular and 1.9 GHz PCS Bands. Forward Link Up to 3.1 Mbps; Reverse Link 1.8 Mbps

# Interface and Online Software Features

Software Delivered by Vendor as a Managed Service

Displays Company Log and Project Name

## Capable of Viewing Actual Live Video

Picture in Picture to View and Control Live Video, While Viewing Additional Data

Robotic Pan, Tilt, Zoom Control of Camera System

Calendar Based Navigation System for Selecting Specific Images

Multifunction Image Browsing

Pan, Tilt and Zoom Capability within a High Definition Image

A Multiview Screen to View All Cameras on Project at the Same Time

Graphical Mark-Up Tools for Detailing and Creating Overlays on Images

Graphical Weather Applet Displaying Ten Points of Local Weather Data and 48-hour Forecast

Remote Solar Monitoring Screen Displaying the DC Amperage Output of Solar Panels

Remote Battery Monitoring Screen Displaying Battery Voltage, Temperature and Status

Remote Cellular Monitoring Screen Displaying Connectivity, Network Traffic and Modem Temperature

Remote Wireless Radio Monitoring Screen Displaying Connectivity, Network Traffic and

Google Map Features Including Wireless Radio Locations

Share Image Tools: Save, Print, Email and Post to Message Board or Mobile Devices

Automated Progress Report in PowerPoint, Open Office and PDF Formats

Map, Aerial and Satellite View by Google

Time-Lapse Feature Includes – Instant Time-Lapse Play Back by Day, Week, Month or Year

Machine to Machine Self-Healing Technology Automates Maintenance of Camera Up to 288 Times Daily

Account Security Features Include – Four Levels of Password Protection, IP Address Block/ Permission and SSL Protection of User Login Password

All Images are the Copyright of the Client and Protected on Secure Servers Owned and Operated by the

System Vendor

# Text boxes

### Product Features

Self-powered lightweight trailer system.

· Standalone wireless and self powered system is easy to

deploy and setup
· Robotic 340° rotation lightweight dome camera
· 12x optical/ 4x digital zoom
· 3G/4G modem
· 30' telescoping mast
· 130 Watt solar panels
· Flooded battery, 50 Amp battery charger
· Real-time remote data management
· Fast, dependable, solid state Linux system
· Custom branding to display your company logo

· Lease or purchase

#### Architectural & Engineering Specifications

#### Product:  ECCS09201

#### Revised:  05-18-2011

#### DOWNLOAD ELECTRONIC VERSION OF THIS SPECS

#### http://www.earthcam.net/aespecs/trailercamlite

For additional EarthCam A&E specs visit: http://www.earthcam.net/aespecs/systems