# Mobile TrailerCam

Combines rapid deployment with self-generated solar power and wireless communications for portable and secure video transmission.

EarthCam Mobile TrailerCam Specification   			         A&E Short Form *

- Physical

Dimensions: 16.2’ L x 7.5’ W x 6.9’ H (4.9m L x 2.3m W x 2.1m H)

Weight: 2800lbs (1270kg)

- Construction

Single Torsion-type Axle Steel Welded Trailer with 2” Adjustable Ball Hitch Manual Outriggers

DOT Approved Lighting Package to Include Brake and Marker Lights

Trailer Mounted Locking Manual/Motorized 30-Foot Telescoping Mast with Spiral Conduit for Cable Deployment

Full Size Spare Tire

- Battery Bank

Charge Controller with Remote Monitoring

Twelve 6Volt DC Deep Cycle Batteries

      - Charge controller with remote monitoring

      - 75 Amp AC Charger

- Solar Array

520 Watt Solar Array made up of Four 130 Watt (Monocrystalline) Silicon Photovoltaic Modules

Region of Operation: Contiguous United States

Autonomy: up to 4 Days Battery Backup

- Camera

Built-in a Stainless Steel  and Polycarbonate Pressurized Dome Enclosure, pressurized to 8 psig (55kPA)

Solid State Internal Temperature, Pressure and dew point sensors for enclosure environmental status monitoring

Meets NEMA 6P and IP67 weatherproof standards

    - Integrated high-resolution camera and lens assembly with a 1/4” EXview HAD(Hole-Accumulation Diode) image sensor

      - Auto Features such as White Balance, Iris Control, Motion Detection, Image Enhancement,

      - Electronic Image Stabilization

      - 768 x 494 Resolution

      - Lens: F/1.4 ,  3.4mm – 119mm

      - 35X Optical and 12X Digital Zoom

      - 360° Continuous Pan, +2° to -92° Tilt

      - Dynamic or Static IP Addressing

      - Camera Enclosure Dimensions: 10.5”Diameter x 11.63”H (267mmx295mm)

      - Operational Temperature: - 40°F to 122°F (- 40°C to 50°C)

Camera Weight: 16 lbs (7.26 kg)

# Communication

Wireless GPS Modem EV–DO Rev. A Full Duplex Transceiver with Dual-Band Support for Both 800 MHz Cellular and

1.9 GHz PCS Bands. Forward Link Up to 3.1 Mbps; Reverse Link 1.8 Mbps and Real Time GPS Reporting

# Interface and Online Software Features

Software Delivered by Vendor as a Managed Service

Displays Company Logo and Project Name

## Capable of Viewing Actual Live Video

Picture in Picture to View and Control Live Video, While Viewing Additional Data

Robotic Pan, Tilt, Zoom Control of Camera System

Calendar Based Navigation System for Selecting Specific Images

##### Multifunction Image Browsing

##### Pan, Tilt and Zoom Capability within a High Definition Image

A Multiview Screen to View All Cameras on Project at the Same Time

Graphical Mark-Up Tools for Detailing and Creating Overlays on Images

Graphical Weather Applet Displaying Ten Points of Local Weather Data and 48-hour Forecast

Remote Solar Monitoring Screen Displaying the DC Amperage Output of Solar Panels

Remote Battery Monitoring Screen Displaying Battery Voltage, Temperature and Status

Remote Cellular Monitoring Screen Displaying Connectivity, Network Traffic and Modem Temperature

Remote Wireless Radio Monitoring Screen Displaying Connectivity, Network Traffic and

Google Map Features Including Wireless Radio Locations

Share Image Tools: Save, Print, Email and Post to Message board or Mobile Devices

Automated Progress Report in PowerPoint, Open Office and PDF Formats

Map, Aerial and Satellite View by Google

Time-Lapse Feature Includes – Instant Time-Lapse Play Back by Day, Week, Month or Year

Machine to Machine Self-Healing Technology Automates Maintenance of Camera Up to 288 Times Daily

Account Security Features Include – Four Levels of Password Protection, IP Address Block/ Permission and SSL Protection of User Login Password

All Images are the Copyright of the Client and Protected on Secure Servers Owned and Operated by the System Vendor

# Text boxes

### Product Features

Real time monitoring and documentation.

· Robotic 360° dome camera with 35x optical zoom
· GPS 3G/4G modem
· 30' telescoping mast
· 130 Watt solar panels
· AGM sealed battery, 75 Amp battery charger
· Full size spare tire and removable tongue
· Real-time remote data management
· Fast, dependable, solid state Linux system
· Custom branding to display your company logo

· Lease or purchase

#### Architectural & Engineering Specifications

#### Product:  ECCS09200

#### Revised:  06-12-2012

#### DOWNLOAD ELECTRONIC VERSION OF THIS SPECS

#### http://www.earthcam.net/aespecs/trailercam

#### For additional EarthCam A&E specs visit: http://www.earthcam.net/aespecs/systems