# 16 MegapixelCam Advanced

Our best HD/live video fixed position camera with maintenance-free wiper.

#### EarthCam 16 MegapixelCam Advanced Specification                                 A&E Short Form*

# Physical

Dimensions: Camera Enclosure: 6.9” (175mm) W x 6.6” (168mm) H x 19.4” (493mm) L

Pan/Tilt Unit: 7.0” (178mm) W x 10.5” (274mm) H x 6.4” (163mm) D

Weight: Camera Enclosure: 13lb (5.9kg), Pan/Tilt Unit: 12lb (5.4kg)

# Environmental

Operational Temperature:  -10°F to +120°F (-23°C to + 49°C)

Thermostatically Controlled Heater and Blower

- Construction

Built-In Aluminum and Epoxy Powder Painted, Weatherproof Standard IP66/IP67

Body Constructed from Extruded Aluminum and Die-Cast Aluminum End-Cover Plates

Weatherproof Feature is Maintained by 2 EPDM-Rubber End Gaskets between Cover Plates and 3 Cable Glands

- Camera

Imager: 16.2 Megapixels (4928 x 3264 Pixels), 15.6mm x 23.6mm CMOS Image Sensor

Lens: F/3.5-5.6, 18mm - 55mm, 3x Optical

Auto Features:  ISO, Shutter, White Balance and Focus

Video Compression: Motion JPEG, Preview: 640 x 426 Streaming Video Resolution

Communication: 10base-T/100base-TX Ethernet, IP Addressing: Dynamic or Static

Designed For “EarthCam Control Center - Megapixel Edition – Fixed with Mobile Support” Software

- Electrical

Operational Voltage: 120VAC (230VAC Available). Power Consumption: 130W

# Interface and Online Software Features

Software Delivered by Vendor as a Managed Service

Displays Company Logo and Project Name

## Capable of Viewing Actual Live Video

HD Snapshot on Demand: HDR (High Dynamic Range) Imaging and Additional Special Effects Including Architectural Miniature, Artistic Color Sketch and Cinematic Black & White

Picture in Picture to View Live Video, While Viewing High Definition Images

Calendar Based Navigation System for Selecting Specific Images

Multifunction Image Browsing

Pan, Tilt and Zoom Capability within a High Definition Image

Access Advanced Camera Settings Including ISO, White Balance and Picture mode

Onscreen Control Button for Wiper Control to Allow Remote Cleaning of the Viewing Window

A Multiview Screen to View All Cameras on Project at the Same Time

Graphical Mark-Up Tools for Detailing and Creating Overlays on Images

Graphical Weather Applet Displaying Ten Points of Local Weather Data and 48-hour Forecast

Remote Solar Monitoring Screen Displaying the DC Amperage Output of Solar Panels

Remote Battery Monitoring Screen Displaying Battery Voltage, Temperature and Status

Remote Cellular Monitoring Screen Displaying Connectivity, Network Traffic and Modem Temperature

Remote Wireless Radio Monitoring Screen Displaying Connectivity, Network Traffic and

Google Map Features Including Wireless Radio Locations

Share Image Tools: Save, Print, Email and Post to Message board or Mobile Devices

Automated Progress Report in PowerPoint, Open Office and PDF Formats

Map, Aerial and Satellite View by Google

Time-Lapse Feature Includes – Instant Time-Lapse Play Back by Day, Week, Month or Year

Machine to Machine Self-Healing Technology Automates Maintenance of Camera Up to 288 Times Daily

Account Security Features Include – Four Levels of Password Protection, IP Address Block/ Permission and SSL Protection of User Login Password

All Images are the Copyright of the Client and Protected on Secure Servers Owned and Operated by the System Vendor

# Text boxes

### Product Features

Our top-of-the-line megapixel camera features live streaming view and

superior HD images for time-lapse photography.

· 16 Megapixel HD fixed position camera: 4928 x 3264

· 640 x 426 live streaming video preview

· Digital presets and Pan/Tilt/Zoom within captured image

· Nikon optics for superior quality

· HDR (High Dynamic Range) imaging and additional special effects

including Architectural Miniature, Artistic Color Sketch and

Cinematic Black & White

· Access advanced camera settings including ISO, white balance and

picture mode

· Take and share on demand snapshot: 16MP, 9MP and 4MP

· Housed in a thermostatically regulated, corrosion-resistant

black enclosure

· Maintenance-free wiper to ensure clear images

· Unique double locking mount for jitter-free documentation

· Fast, dependable, solid state Linux system

· Transmit over new fast 4G wireless networks

#### Architectural & Engineering Specifications

#### Product:  ECCS03209

Revised:  09-05-2012

#### DOWNLOAD ELECTRONIC VERSION OF THIS SPECS

#### http://www.earthcam.net/aespecs/megapixelcamadvanced

For additional EarthCam A&E specs visit: http://www.earthcam.net/aespecs/systems