EARTHCAM Broadcastcam

PRODUCT

MANUFACTURER

EarthCam, Inc.

800.EarthCam (327.8422) toll free

201.488.1111 voice

201.488.1119 fax

84 Kennedy Street,

Hackensack, NJ 07601.

www.EarthCam.net

GENERAL DESCRIPTION

The Robotic 24/7 H.264 High Definition streaming video camera system transmits multiple, individually configured, simultaneous video streams at full frame rate. Perfect for billboard monitoring/video surveillance systems where clear images and greater detail are required with the added benefit of maximum pan, tilt zoom flexibility.

SYSTEM REQUIRMENTS

The indoor/outdoor camera system shall consist of a weatherproof aluminum constructed housing, HD streaming camera to be mounted on a fixed pole, wall, parapet or ceiling.

The camera shall have the ability to take digital still images every 5 or 60 minutes, depending on service package, as well as provide live video.

The camera shall upload both High Definition images and video over a wireless cellular modem, a wireless point-to-point system or a RJ-45 hardwired connection to a DSL or cable modem.

The content shall be sent to a secure, password protected website with an Interface and Online Software features provided by the Vendor as a Managed Service.

The system shall operate on 120VAC and have a maximum power consumption of  35W.

EQUIPMENT

HD Camera system: H.264 streaming video camera system with live streaming video and lens assembly consisting of a charge coupled device (CMOS) camera with a remotely controlled focal lens with the following features:

Image sensor: 1/3” Progressive scan CMOS 2 Megapixel

Lens: F5.1 – 51mm, F1.8 – 2.1, Auto day/night IR filter, Autofocus

Sensitivity: Color 2 lux at 30IRE, F1.8, B/W: 0.2 lux at 30IRE, F1.8

Shutter time:1/10000s to 1/2s

Video Compression: H.264 (MPEG-4 Part 10/AVC); Motion JPEG

Resolution: HDTV 1080i 1920x1080; HDTV 720p 1280x720

Frame rate H.264: 30/25 fps in all resolutions

Frame rate Motion JPEG: 30/25 fps in all resolutions

Video streaming: Multi-stream and Motion JPEG: simultaneous, individually configured streams in max. resolution at 25/30 fps

Image settings: Compression, brightness, sharpness, white balance, exposure control, blacklight compensation, rotation, mirroring of images, Text and image overlay

Security: Password protection, IP address filtering, HTTPS encryption, IEEE 802.1X network access control, digest authentication user access log

Processor and memory: ARTPEC-3, 256 MB RAM 128MB Flash

Connectors: RJ45 10BASE_T/ 100BASE_TX PoE

Cable entry: UL rated Compression glands/ 32-pin Military Connector (MIL-C-26482).

Window wiper: Remotely controlled

Weather Proof Enclosure (IP66 rated)

Operating temperature: -10°F to 120°F (-23°C to 49°C)

Dimensions: 6.9" W x 20.2” L x 5.2” H (17.6cm x 51.4cm x 13.1cm)

Weight: 14 lbs (6.35kg).

Operating voltage: 120VAC / 230VAC 50/60hz available.

Designed for the “EarthCam Control Center - Streaming Video Edition - Fixed with Mobile Support” software.”

Robotic Pan/Tilt Pedestal: Aluminum Pan/Tilt with stainless steel hardware, factory applied black powder coat and completely gasketed and sealed robotic pedestal with the following features:

Pan Range: 435º (+/- 217.5º).

Tilt Range: 90º (+/- 45º).

Backlash: Adjustable to 0º.

Repeatability of 0.25º.

Dimensions: 7.0”  W x 10.5” H x 6.4” D (17.8cm x 27.4cm x 16.3cm)

Weight: Pan/Tilt Unit: 12lb (5.4kg)

Operational Temperature: -10°F to 120°F (-23°C to 49°C).

Data Connection: Provide one of the following:

In areas with cellular coverage, operate cameras via built-in cellular data connection provided and maintained by the system vendor.

In areas without cellular coverage, operate cameras via an RJ-45 Ethernet data connection over broadband or satellite Internet access provided and maintained by the Contractor.

Quantity of Cameras: As required by Owner.

INTERFACE AND ONLINE SOFTWARE

INTERFACE AND ONLINE SOFTWARE

Remote Access: Contractor’s System Vendor shall provide an internet based interface and online software as a managed service, to allow the viewing of all high-definition digital still images captured and stored and live video, from any location with internet access via a secure password protected website.

Maintain images on the System Vendor’s website for reference available at all times during the life of the project and for not less than 60 days after completion.

Online Interface Features:

Software delivered by Vendor as a Managed Service.

Displays Company logo and project name.

Capable of viewing actual live video.

Picture in Picture to view live video, while viewing high definition images.

Calendar based navigation system for selecting specific images.

Multifunction image browsing.

Pan, tilt and zoom control capability within a high-definition image.

Onscreen button for wiper control to allow remote cleaning of the viewing window.

A multi-view screen to view all of the cameras on a project at the same time.

Graphical mark-up tools for detailing and creating overlays on images.

Graphical weather applet displaying ten points of local weather data and 48-hour forecast.

Remote Solar Monitoring Screen Displaying the DC Amperage Output of Solar Panels.

Remote Battery Monitoring Screen Displaying Battery Voltage, Temperature and Status.

Remote cellular monitoring screen displaying connectivity, network traffic and modem temperature.

Remote wireless radio monitoring screen displaying connectivity, network traffic and Google Map features including wireless radio locations.

Share image tools: save, print, email and post to message board or mobile devices.

Automated progress reports in Power Point, Open Office and PDF formats.

Map, aerial and satellite view by Google.

Time lapse features include – Instant time lapse play back by day, week, month or year.

Machine to machine self-healing technology that automates maintenance of camera up to 288 times daily.

Account security features include – Four levels of password protection, IP address block/ permission and SSL protection of the user login password.

All Images are the Copyright of the Client and Protected on Secure Servers Owned and Operated by the System Vendor.

EXECUTION

INSTALLATION

Installation should be performed by qualified service personnel only in accordance with National Electrical codes or applicable local codes.

Install camera system following with manufacturer’s included instruction manual.

Camera system including physical accessories and mounting equipment shall remain the owners property.

END OF SECTION