SECTION 01 32 34.01 – EARTHCAM CONSTRUCTIONCAM HD

PRODUCT

MANUFACTURER

EarthCam, Inc.

800.EarthCam (327.8422) toll free

201.488.1111 voice

201.488.1119 fax

650 E Crescent Ave,

Upper Saddle River, NJ 07458.

www.EarthCam.net

GENERAL DESCRIPTION

The fixed position 24/7 H.264 High Definition streaming video camera system transmits multiple, individually configured, simultaneous video streams at full frame rate.

SYSTEM REQUIRMENTS

The indoor/outdoor camera system shall consist of a die-cast and extruded aluminum housing, HD streaming camera to be mounted on a fixed pole, wall, parapet or ceiling.

The camera shall have the ability to take digital still images every 5 to 60 minutes, depending on service package, as well as provide live video.

The camera shall upload both High Definition images and video over a wireless cellular modem, a wireless point-to-point system or a RJ-45 hardwired connection to a DSL or cable modem.

The content shall be sent to a secure, password protected website with an Interface and Online Software features provided by the Vendor as a Managed Service.

The system shall operate on 120VAC and have a maximum power consumption of 36W.

EQUIPMENT

Camera: H.264 streaming video camera system with live streaming with a remotely controlled focal lens with the following features:

Image Sensor	1/3” Progressive scan CMOS 2 Megapixel

Lens	F=5.1 – 51mm, f/1.8 – 2.1, autofocus, auto day/night

Color Illumination	Color: 2 lux at 30 IRE, f/1.8

B/W: 0.2 lux at 30IRE, f/1.8

Shutter time 	1/10000s to 1/2s

Video compression	H.264, MPEG-4 Part 10/AVC, Motion JPEG

Resolution	HDTV 1080i 1920x1080

HDTV 720p 1280x720

Frame rate	30fps in all resolutions

Video streaming 	Multi-stream H.264 and Motion JPEG

Image settings	Compression, brightness, white balance, exposure control, backlight compensation, rotation, mirroring of images, text and image overlay

Security 	Password protection, IP address filtering, HTTPS encryption, IEEE 802.1X network access control

Processor and memory	ARTPEC-3, 256 MB RAM 128MB Flash

Connectors 	RJ-45 10BASE-T/100BASE-TX PoE

Camera Enclosure:

Enclosure	Die-cast and extruded aluminum housing

Cable Entry	3 removable cable glands

Window wiper	Remotely controlled

Pan and Tilt Robotic Base: Operator controlled movement for pan/tilt functionality, IP66-rated protection, easily panned and tilted by operator:

Pan Range				0° to 355°

Tilt Range				10° to -80°

Overall System:

Operating temperature	-10°F to 120°F (-23°C to 49°C)

Camera Enclosure Dimensions	6.3” (160mm) H x 6.9” (176mm) W x 20.2” (514mm) D

Pan/Tilt Unit Dimensions	11.3” (288mm) H x 6.5” (165mm) W x 7.4” (189mm) D

Camera Enclosure Weight	31lb (5.9kg)

Pan/Tilt Unit Weight	9lb (4.1kg)

Operational Voltage			24VAC (100-240VAC 50/60Hz Available)

Maximum Power Consumption	36W

Designed for the “EarthCam Control Center - Streaming Video Edition - Robotic with Mobile Support” software.

Quantity of Cameras: As required by owner.

INTERFACE AND ONLINE SOFTWARE

Remote Access: Contractor’s System Vendor shall provide an internet based interface and online software as a managed service, to allow the viewing of all high-definition digital still images captured and stored and live video, from any location with internet access via a secure password protected website.

Maintain images on the System Vendor’s website for reference available at all times during the life of the project and for not less than 60 days after completion.

Online Interface Features:

Software delivered by vendor as a managed service.

Displays Company logo and project name.

Capable of viewing actual live video.

Picture in Picture to view live video, while viewing high definition images.

Calendar based navigation system for selecting specific images.

Multifunction image browsing.

Pan, tilt and zoom control capability within a high-definition image.

Onscreen button for wiper control to allow remote cleaning of the viewing window.

A multiview screen to view all of the cameras on a project at the same time.

Graphical mark-up tools for detailing and creating overlays on images.

Graphical weather applet displaying ten points of local weather data and 48-hour forecast.

Remote solar monitoring screen displaying the DC amperage output of solar panels.

Remote battery monitoring screen displaying battery voltage, temperature and status.

Remote cellular monitoring screen displaying connectivity, network traffic and modem temperature.

Remote wireless radio monitoring screen displaying connectivity, network traffic and Google Map features including wireless radio locations.

Share image tools: save, print, email and post to message board or mobile devices.

Automated progress reports in PowerPoint, OpenOffice and PDF formats.

Map, aerial and satellite view by Google.

Time lapse features include – Instant time lapse play back by day, week, month or year.

Machine to machine self-healing technology that automates maintenance of camera up to 288 times daily.

Account security features include – Four levels of password protection, IP address block/ permission and SSL protection of the user login password.

All images are the copyright of the client and protected on secure servers owned and operated by the system vendor.

EXECUTION

INSTALLATION

Installation should be performed by qualified service personnel only in accordance with National Electrical codes or applicable local codes.

Install camera system following with manufacturer’s included instruction manual.

Camera system including physical accessories and mounting equipment shall remain the owner’s property.

END OF SECTION